## Slide 1: Expanding Energy Efficiency for BC Hydro: Lessons from Industry Leaders June 19, 2012
Prepared for the BC Sustainable Energy Association

## Slide 2: Overview
Key Terms and Concepts
BC Hydro’s IRP
US Data on Energy Efficiency
GEEG’s Empirical Research and Analysis
Predicting Efficiency Costs for BC Hydro
Impact of Expanded Efficiency for BC Hydro
Program Enhancements

## Slide 3: 1. Key Terms and Concepts

## Slide 4: Types of Savings
kW
Year 1
Year 2
Year 3
Usage before EE
Annual Peak Demand
Savings (kW-yr)
Annual Energy Savings (kWh-yr)
Usage after EE

## Slide 5: Savings Depth (%)
kWh-yr
Year 1
Year 2
Year 3
Sales
Savings
÷
Annual Sales
Annual Savings

## Slide 6: Why Use Sales as Basis for Depth?
Annual sales correlates more closely to the size of efficiency opportunities.
Growth rates more volatile.
Why not use sales growth rate as basis for savings depth?

## Slide 7: Savings Tiers
Tier | Definition
Tier 1 | Savings Depth ≥ 1.5% Target = 2%
Tier 2 | 1.5% > Savings Depth ≥ 0.67% Target = 1%
Tier 3 | 0.67% > Savings Depth ≥ 0.33% Target = 0.5%
Tier 4 | 0.33% > Savings Depth Target = 0.25%

## Slide 8: Unit Costs vs Levelized Costs
Initial Cost
$$$
=
Many years of savings
kWh-yr
Year 1
kWh-yr
Year 2
kWh-yr
Year 3
kWh-yr
Year N
…
Amortize the cost over
the period of savings to get
Divide cost by annual
savings to get
Unit Costs ($/kWh-yr)
Levelized Costs ($/kWh)

## Slide 9: Example Levelized Cost Calculation
Unit Cost = $0.30/kWh-yr
Lifetime = 15 years
Real Discount Rate = 5.5%
Levelized Cost =
Given:
Spread the initial cost over the life of the savings, similar to an annual payment on a $0.30 loan for 15 years at 5.5%
= $0.0299/kWh
A cost now comparable to supply-side resources.
Slide was added after the presentation, for purposes of clarity.

## Slide 10: Economies of Scale vs. Diminishing Returns
Economies of Scale
  Lower fixed costs as a percentage of total spending
Diminishing Returns
  More expensive measures for deeper savings
  Higher incentives required for everyone to get additional participants

## Slide 11: Economies of Scale vs. Diminishing Returns (cont.)
Savings as a Percentage of Sales
Cost of
Energy
Savings
As a portfolio ramps up,
economies of scale drive down costs
Beyond a certain point,
the law of diminishing
returns pushes costs up

## Slide 12: Cost-effectiveness Tests
Benefit/Cost | Description | TRC | PAC
Cost | Administration Costs | X | X
Cost | Participant Costs | X | 
Cost | Customer Incentives |  | X
Benefit/Cost | Description | TRC | PAC
Benefit | Avoided Electric Costs | X | X
Benefit | Avoided Gas Costs | X | X
Benefit/Cost | Description | TRC | PAC
TRC = Total Resource Cost Test
PAC = Program Administrator Cost Test (“Utility Cost Test”)

## Slide 13: Cost of Energy Savings TRC vs PAC

## Slide 14: 2. BC Hydro’s Latest IRP

## Slide 15: BCHydro Projected Savings
Chart: BCH Planned Energy-Focused DSM Program Cumulative Savings (From F2012)
| F2014 | F2015 | F2016 | F2017 | F2018 | F2019 | F2020 | F2021 | F2022
GWh | 1363 | 1865 | 2355 | 2925 | 3445 | 4033 | 4615 | 5216 | 5676
MW | 179 | 240 | 299 | 369 | 428 | 490 | 566 | 642 | 702

## Slide 16: BCHydro Savings % of Sales
Chart: Energy-Focused DSM Incremental Savings % of Sales
| F2013 | F2014 | F2015 | F2016 | F2017 | F2018 | F2019 | F2020 | F2021
 | 0.0052123 | 0.0063471 | 0.0088219 | 0.0082323 | 0.0089733 | 0.0078351 | 0.0086955 | 0.0084684 | 0.0086535

## Slide 17: BCHydro Projected Costs
Chart: Energy-Focused DSM Program Spending and Savings
| F2013 | F2014 | F2015 | F2016 | F2017 | F2018 | F2019 | F2020 | F2021
Budgets | 135.8018 | 273.4109 | 281.5908 | 270.3912 | 281.6023 | 295.6963 | 318.4065 | 268.7283 | 296.5073
$/kWh-yr | 0.49365 | 0.78335 | 0.56094 | 0.55182 | 0.49404 | 0.56865 | 0.54151 | 0.46173 | 0.49336

## Slide 18: 3. US Data on Energy Efficiency

## Slide 19: Electric Energy Savings in the US by Sector (from US EIA)

## Slide 20: ACEEE Costs and Savings for States, 2006 and 2007
Source: American Council for an Energy Efficient Economy
Tier 1
Tier 2
Tier 3
Tier 4
-yr
Grouping in Tiers 2 & 4
General range of
$0.10 - $0.30
Unit Cost (2011$/kWh-yr)

## Slide 21: 4. GEEG’s Empirical Research and Analysis

## Slide 22: Data Collected
Incremental annual energy savings and spending for residential and non-residential sectors where possible
Covering:
  23 States and 2 Canadian Provinces
  37 Program Administrators
  470 Program Years of Data
  $25 Billion of Spending (2011$)
  105,000 GWh/y of Cumulative Annual Savings

## Slide 23: Collected Data by Savings Tier
Tier | Definition | Observations
Tier 1 | Savings ≥ 1.5% Target = 2% | Includes 9 program-years since 2005 from VT, CA, and CT.
Tier 2 | 1.5% > Savings ≥ 0.67% Target = 1% | 60 program-years fall in this tier, including IA, ME, MA, NV, NY, RI, HI, the Pacific Northwest, British Columbia, and Nova Scotia
Tier 3 | 0.67% > Savings ≥ 0.33% Target = 0.5% | States in this tier include AR, NJ, and WI
Tier 4 | 0.33% > Savings > 0 Target = 0.25% | States in this tier include OK and TX.

## Slide 24: Historic Values
Convergence
Most in Tier 2
Unit Cost (2011$/kWh-yr)

## Slide 25: Planned Values
Unit Cost (2011$/kWh-yr)
Trend higher

## Slide 26: Regression Model
Conducted multiple regression on dataset testing correlation between resource acquisition costs and:
  Savings Depth (% Savings)
  Time
  Customer Sector
  Location
Results:
  Adjusted R2 = 0.875 (model accounts for all but 13.5% of sample variance in costs)
  Highly statistically significant variables (≥ 99.9% confidence-level)

## Slide 27: Effects of Savings Depth on Resource Acquisition Costs

## Slide 28: Diminishing Returns over Time
Each additional year of maturity adds $0.075/kWh-y to the costs
Planned savings add $0.072/kWh-y to costs
Some locations have higher acquisition costs. Being in
  California adds $0.17/kWh-y
  New England adds $0.20/kWh-y

## Slide 29: 5. Predicting Efficiency Costs for BC Hydro

## Slide 30: Overview of Approach

## Slide 31: General Assumptions
Ramp up to 2.0% by 2014
Savings as a % of Sales
Savings Goals
Load forecast from IRP

## Slide 32: Efficiency Resource Acquisition Costs
Chart: Tier 1 Spending per kWh-yr Savings
| 2013.0 | 2014.0 | 2015.0 | 2016.0 | 2017.0 | 2018.0 | 2019.0 | 2020.0 | 2021.0 | 2022.0 | 2023.0 | 2024.0 | 2025.0 | 2026.0 | 2027.0 | 2028.0 | 2029.0 | 2030.0 | 2031.0 | 2032.0
Residential | 0.33167 | 0.3009 | 0.30913 | 0.31736 | 0.32559 | 0.33382 | 0.34205 | 0.35027 | 0.3585 | 0.36673 | 0.37496 | 0.38319 | 0.39142 | 0.39965 | 0.40787 | 0.4161 | 0.42433 | 0.43256 | 0.44079 | 0.44902
C&I | 0.25649 | 0.22572 | 0.23395 | 0.24218 | 0.25041 | 0.25864 | 0.26687 | 0.27509 | 0.28332 | 0.29155 | 0.29978 | 0.30801 | 0.31624 | 0.32447 | 0.33269 | 0.34092 | 0.34915 | 0.35738 | 0.36561 | 0.37384

## Slide 33: 6. Impact of Expanded Efficiency for BC Hydro

## Slide 34: Tier 1 Savings Scenario
Year | Incremental GWh Savings | Incremental MW Savings | Budgets (Millions 2011$)
Incremental Annual |  |  | 
2013 | 766 | 143 | $ 217.56
2014 | 1,063 | 198 | $ 268.62
2015 | 1,106 | 205 | $ 287.88
2016 | 1,145 | 213 | $ 306.99
2017 | 1,198 | 220 | $ 330.20
2018 | 1,279 | 235 | $ 361.51
2019 | 1,336 | 245 | $ 387.97
2020 | 1,361 | 250 | $ 406.64
2021 | 1,382 | 254 | $ 424.40
2022 | 1,398 | 256 | $ 441.02

## Slide 35: Tier 1 Savings Scenario
Year | Cumulative GWh Savings | Cumulative MW Savings | Cumulative Budgets (Millions 2011$)
Cumulative Annual |  |  | 
2013 | 1,455 | 271 | $ 352.17
2014 | 2,469 | 460 | $ 620.79
2015 | 3,466 | 642 | $ 908.67
2016 | 4,463 | 829 | $ 1,215.67
2017 | 5,481 | 1,005 | $ 1,545.87
2018 | 6,514 | 1,195 | $ 1,907.37
2019 | 7,465 | 1,369 | $ 2,295.34
2020 | 8,371 | 1,535 | $ 2,701.98
2021 | 9,228 | 1,693 | $ 3,126.38
2022 | 10,017 | 1,837 | $ 3,567.40

## Slide 36: Cumulative Budgets
Chart: Cumulative Spending
| 2012.0 | 2013.0 | 2014.0 | 2015.0 | 2016.0 | 2017.0 | 2018.0 | 2019.0 | 2020.0 | 2021.0 | 2022.0
Tier 1 | 134.6089 | 352.1729 | 620.7922 | 908.6735 | 1215.6658 | 1545.8666 | 1907.3716 | 2295.3377 | 2701.9793 | 3126.378 | 3567.3973
BCH Planned Energy-Focused DSM | 134.6089 | 270.4107 | 543.8215 | 825.4123 | 1095.8035 | 1377.4058 | 1673.1022 | 1991.5087 | 2260.2369 | 2556.7442 | 2804.1884

## Slide 37: Energy Requirements vs. Supply Resources
Chart: Forecasts (with line losses)
| 2012.0 | 2013.0 | 2014.0 | 2015.0 | 2016.0 | 2017.0 | 2018.0 | 2019.0 | 2020.0 | 2021.0 | 2022.0 | 2023.0 | 2024.0 | 2025.0 | 2026.0 | 2027.0 | 2028.0 | 2029.0 | 2030.0 | 2031.0
Base Case (w/o Energy-Focused DSM) | 56728.2134 | 58080.5387 | 60021.6468 | 61712.7307 | 64286.4934 | 68166.8238 | 70874.1279 | 72038.8467 | 73112.4045 | 73984.2458 | 75032.5973 | 75913.285 | 76658.0338 | 77283.9443 | 76746.9675 | 77820.9248 | 78861.8872 | 79702.4354 | 80804.0394 | 82221.2903
Base Case (w/ BCH Planned DSM) | 55915 | 56965 | 58523 | 59663 | 61700 | 64958 | 67097 | 67617 | 68052 | 68264 | 68807 | 69286 | 69727 | 70118 | 69385 | 70257 | 71121 | 71955 | 73047 | 74493
Including DSM: Tier 1 | 55915 | 56479.2498 | 57307.1902 | 57903.8659 | 59385.1792 | 62154.426 | 63731.6262 | 63853.9616 | 63933.3736 | 63864.6312 | 64045.7237 | 64076.9292 | 64012.5257 | 63861.131 | 62601.4498 | 63191.201 | 63788.0166 | 64275.8559 | 65041.521 | 66134.3307
Supply Resources | 57938 | 61448 | 61888 | 64009 | 63867 | 64197 | 64497 | 63862 | 63674 | 63329 | 62925 | 62682 | 62499 | 62089 | 62018 | 62019 | 62016 | 62016 | 62016 | 62016

## Slide 38: Peak Requirements vs. Supply Resources
Chart: Forecasts (with line losses)
| 2012.0 | 2013.0 | 2014.0 | 2015.0 | 2016.0 | 2017.0 | 2018.0 | 2019.0 | 2020.0 | 2021.0 | 2022.0 | 2023.0 | 2024.0 | 2025.0 | 2026.0 | 2027.0 | 2028.0 | 2029.0 | 2030.0 | 2031.0
Base Case (w/o Energy-Focused DSM) | 10602.7976 | 10780.5014 | 11161.8142 | 11416.7723 | 11941.3913 | 12498.8055 | 12567.2629 | 12660.244 | 12773.626 | 12856.064 | 12978.9735 | 13157.7882 | 13301.4991 | 13461.4687 | 13525.2067 | 13636.4906 | 13806.5126 | 13940.4475 | 14103.1547 | 14293.3432
Base Case (w/ BCH Planned DSM) | 10496 | 10634 | 10965 | 11153 | 11613 | 12094 | 12098 | 12123 | 12153 | 12152 | 12209 | 12335 | 12438 | 12566 | 12604 | 12691 | 12840 | 12976 | 13143 | 13342
Including DSM: Tier 1 | 10450.3362 | 10482.5809 | 10656.0397 | 10711.6475 | 11030.8314 | 11396.0235 | 11257.1995 | 11158.9887 | 11090.0265 | 10999.9445 | 10963.783 | 10986.7875 | 10982.0852 | 10999.4831 | 10930.6641 | 10953.1359 | 11041.6934 | 11110.9351 | 11212.0251 | 11342.7052
Supply Resources (Net of Reserves) | 11437 | 11574 | 11617 | 11526 | 11132 | 11158 | 11147 | 11089 | 11055 | 10985 | 10985 | 10931 | 10931 | 10907 | 10907 | 10907 | 10906 | 10906 | 10906 | 10906

## Slide 39: Cumulative Energy Savings
Chart: Cumulative GWh Savings
| 2013.0 | 2014.0 | 2015.0 | 2016.0 | 2017.0 | 2018.0 | 2019.0 | 2020.0 | 2021.0 | 2022.0
Tier 1 | 1455.4975 | 2468.7634 | 3465.5933 | 4462.6424 | 5480.595 | 6514.452 | 7465.1257 | 8371.1149 | 9227.5597 | 10016.9497

BCH Energy-Focused Planned DSM | 1013.9731 | 1363 | 1865 | 2355 | 2925 | 3445 | 4033 | 4615 | 5216 | 5676

## Slide 40: Levelized Costs
Sector | Levelized Cost 2012$/MWh | 
 | Min (F2014) | Max (F2032)
Residential | $40.8 | $60.8
Non-Residential | $23.0 | $38.0
Total | $29.3 | $45.9

## Slide 41: 7. Program Enhancements

## Slide 42: Scale up Savings
Increase pace and scale
Target customer sectors
Maximize net benefits

## Slide 43: Avoid
1. Cream-skimming
2. Lost-opportunities
=

## Slide 44: Encourage
Integration of program design and delivery
Across fuels and service areas.

## Slide 45: Go Deeper
Low-income
Residential
Small-to-medium Commercial
Enhance programs to get as much a savings per project
as economically possible
Important sectors include:

## Slide 46: Redesign Incentives

## Slide 47: Convert Street Lighting
LED Street Lights in Foshan, China

## Slide 48: Lead by Example
Long-term capital plan to capture all cost-effectively achievable efficiency

## Slide 49: Questions?
John Plunkett
plunkett@greenenergyeconomics.com
www.greenenergyeconomics.com